## Slide 1: CS 110 Computer Architecture Lecture 11: Pipelining
Instructor:
Sören Schwertfeger
http://shtech.org/courses/ca/
School of Information Science and Technology SIST
ShanghaiTech University
Slides based on UC Berkley's CS61C

## Slide 2: Summary: Single-cycle Processor
Five steps to design a processor:
  1. Analyze instruction set  datapath requirements
  2. Select set of datapath components & establish clock methodology
  3. Assemble datapath meeting the requirements
  4. Analyze implementation of each instruction to determine setting of control points that effects the register transfer.
  5. Assemble the control logic
    Formulate Logic Equations
    Design Circuits
Control
Datapath
Memory
Processor
Input
Output

## Slide 3: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
Clock rate (cycles/second = Hz) = 1/Period (seconds/cycle)
Notes: 1.25 GHz

## Slide 4: Single Cycle Performance
Assume time for actions are
  100ps for register read or write; 200ps for other events
Clock period is?
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps
What can we do to improve clock rate?
Will this improve performance as well?
  Want increased clock rate to mean faster programs
Notes: 1.25 GHz

## Slide 5: Gotta Do Laundry
Ann, Brian, Cathy, Dave each have one load of clothes to wash, dry, fold, and put away
  Washer takes 30 minutes
  Dryer takes 30 minutes
  “Folder” takes 30 minutes
  “Stasher” takes 30 minutes to put clothes into drawers
A
B
C
D

## Slide 6: Sequential Laundry
Sequential laundry takes 8 hours for 4 loads
T
a
s
k
O
r
d
e
r
B
C
D
A
30
Time
30
30
30
30
30
30
30
30
30
30
30
30
30
30
30
6 PM
7
8
9
10
11
12
1
2 AM

## Slide 7: Pipelined Laundry
Pipelined laundry takes 3.5 hours for 4 loads!
T
a
s
k
O
r
d
e
r
B
C
D
A
12
2 AM
6 PM
7
8
9
10
11
1
Time
30
30
30
30
30
30
30

## Slide 8: Pipelining Lessons (1/2)
Pipelining doesn’t help latency of single task, it helps throughput of entire workload
Multiple tasks operating simultaneously using different resources
Potential speedup = Number pipe stages
Time to “fill” pipeline and time to “drain” it reduces speedup: 2.3x (8/3.5) v. 4x (8/2) in this example
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 9: Pipelining Lessons (2/2)
Suppose new Dryer takes 20 minutes, new Folder takes 20 minutes. How much faster is pipeline?
Pipeline rate limited by slowest pipeline stage
Unbalanced lengths of pipe stages reduces speedup
6 PM
7
8
9
Time
B
C
D
A
30
30
30
30
30
30
30
T
a
s
k
O
r
d
e
r

## Slide 10: Execution Steps in MIPS Datapath
1) IFtch: Instruction Fetch, Increment PC
2) Dcd: Instruction Decode, Read Registers
3) Exec: Mem-ref: Calculate Address Arith-log: Perform Operation
4) Mem: Load: Read Data from Memory Store: Write Data to Memory
5) WB: Write Data Back to Register

## Slide 11: Single Cycle Datapath
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back

## Slide 12: Pipeline registers
PC
instruction
memory
+4
rt
rs
rd
registers
ALU
Data
memory
imm
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write Back
Need registers between stages
  To hold information produced in previous cycle

## Slide 13: More Detailed Pipeline

## Slide 14: IF for Load, Store, …

## Slide 15: ID for Load, Store, …

## Slide 16: EX for Load

## Slide 17: MEM for Load

## Slide 18: WB for Load – Oops!
Wrong register number!

## Slide 19: Corrected Datapath for Load

## Slide 20: Pipelined Execution Representation
Every instruction must take same number of steps, so some stages will idle
  e.g. MEM stage for any arithmetic instruction
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
IF
ID
EX
MEM
WB
Time
Notes: Each instruction has identical latency!

## Slide 21: Graphical Pipeline Diagrams
Use datapath figure below to represent pipeline:
IF
ID
EX
Mem
WB
ALU
I$
Reg
D$
Reg
1. Instruction
Fetch
2. Decode/
Register Read
3. Execute
4. Memory
5. Write
Back
PC
instruction
memory
+4
Register
File
rt
rs
rd
ALU
Data
memory
imm
MUX

## Slide 22: Graphical Pipeline Representation
I
n
s
t
r
O
r
d
e
r
Load
Add
Store
Sub
Or
I$
Time (clock cycles)
I$
ALU
Reg
Reg
I$
D$
ALU
ALU
Reg
D$
Reg
I$
D$
Reg
ALU
Reg
Reg
Reg
D$
Reg
D$
ALU
RegFile: left half is write, right half is read
Reg
I$

## Slide 23: Pipelining Performance (1/3)
Use Tc (“time between completion of instructions”) to measure speedup
  Equality only achieved if stages are balanced (i.e. take the same amount of time)
If not balanced, speedup is reduced
Speedup due to increased throughput
  Latency for each instruction does not decrease

## Slide 24: Pipelining Performance (2/3)
Assume time for stages is
  100ps for register read or write
  200ps for other stages
What is pipelined clock rate?
  Compare pipelined datapath with single-cycle datapath
Instr | Instr fetch | Register read | ALU op | Memory access | Register write | Total time
lw | 200ps | 100 ps | 200ps | 200ps | 100 ps | 800ps
sw | 200ps | 100 ps | 200ps | 200ps |  | 700ps
R-format | 200ps | 100 ps | 200ps |  | 100 ps | 600ps
beq | 200ps | 100 ps | 200ps |  |  | 500ps

## Slide 25: Pipelining Performance (3/3)
Single-cycle
Tc = 800 ps
f = 1.25GHz
Pipelined
Tc = 200 ps
f = 5GHz
Notes: Here using Tc as “time between completion of instructions.”

## Slide 26: Question
Logic in some stages takes 200ps and in some 100ps. Clk-Q delay is 30ps and setup-time is 20ps. What is the maximum clock frequency at which a pipelined design can operate?
A: 10GHz
B: 5GHz
C: 6.7GHz
D: 4.35GHz
E: 4GHz
Notes: E

## Slide 27: Administrivia: Midterm I
Date: Friday, Apr. 8
Time: 10:15 - 11:55 (normal lecture slot)
Venue: H2 109 + H2 103
One table per student
Closed book:
  You can bring one A4 page with notes (both sides; Chinese is OK): Write you Chinese and pingying name on the top!
  You will be provided with the MIPS ”green sheet”
  No other material allowed!

## Slide 28: Administrivia: Midterm I
Switch cell phones off! (not silent mode – off!)
  Put them in your bags.
Bags under the table. Nothing except paper, pen, 1 drink, 1 snack on the table!
No other electronic devices are allowed!
  No ear plugs, music, …
Anybody touching any electronic device will FAIL the course!
Anybody found cheating (copy your neighbors answers, additional material, ...) will FAIL the course!

## Slide 29: Question
Which statement is false?
A: Pipelining increases instruction throughput
B: Pipelining increases instruction latency
C: Pipelining increases clock frequency
D: Pipelining decreases number of components

## Slide 30: Pipelining Hazards
A hazard is a situation that prevents starting the next instruction in the next clock cycle
Structural hazard
  A required resource is busy (e.g. needed in multiple stages)
Data hazard
  Data dependency between instructions
  Need to wait for previous instruction to complete its data read/write
Control hazard
  Flow of execution depends on previous instruction

## Slide 31: 1. Structural Hazards
Conflict for use of a resource
MIPS pipeline with a single memory?
  Load/Store requires memory access for data
  Instruction fetch would have to stall for that cycle
    Causes a pipeline “bubble”
Hence, pipelined datapaths require separate instruction/data memories
  Separate L1 I$ and L1 D$ take care of this

## Slide 32: Structural Hazard #1: Single Memory
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Trying to read same memory twice in same clock cycle

## Slide 33: Structural Hazard #2: Registers (1/2)
I$
Load
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)
Can we read and write to registers simultaneously?

## Slide 34: Structural Hazard #2: Registers (2/2)
Two different solutions have been used:
  Split RegFile access in two: Write during 1st half and Read during 2nd half of each clock cycle
    Possible because RegFile access is VERY fast (takes less than half the time of ALU stage)
  Build RegFile with independent read and write ports
Conclusion: Read and Write to registers during same clock cycle is okay
Structural hazards can always be removed by adding hardware resources

## Slide 35: 2. Data Hazards (1/2)
Consider the following sequence of instructions:
add $t0, $t1, $t2
sub $t4, $t0, $t3
and $t5, $t0, $t6
or $t7, $t0, $t8
xor $t9, $t0, $t10

## Slide 36: 2. Data Hazards (2/2)
Data-flow backwards in time are hazards
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
I
n
s
t
r
O
r
d
e
r
Time (clock cycles)

## Slide 37: Data Hazard Solution: Forwarding
Forward result as soon as it is available
  OK that it’s not stored in RegFile yet
sub $t4,$t0,$t3
ALU
I$
Reg
D$
Reg
and $t5,$t0,$t6
ALU
I$
Reg
D$
Reg
or $t7,$t0,$t8
I$
ALU
Reg
D$
Reg
xor $t9,$t0,$t10
ALU
I$
Reg
D$
Reg
add $t0,$t1,$t2
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Notes: Also: register bypassing

## Slide 38: Datapath for Forwarding (1/2)
What changes need to be made here?

## Slide 39: Datapath for Forwarding (2/2)
Handled by forwarding unit
Notes: Scan figure 4.54 on p. 368.

## Slide 40: Data Hazard: Loads (1/4)
Recall: Dataflow backwards in time are hazards
Can’t solve all cases with forwarding
  Must stall instruction dependent on load, then forward (more hardware)
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
lw $t0,0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg

## Slide 41: Data Hazard: Loads (2/4)
Hardware stalls pipeline
  Called “hardware interlock”
sub $t3,$t0,$t2
ALU
I$
Reg
D$
Reg
bubble
and $t5,$t0,$t4
ALU
I$
Reg
D$
Reg
bubble
or $t7,$t0,$t6
I$
ALU
Reg
D$
bubble
lw $t0, 0($t1)
IF
ID/RF
EX
MEM
WB
ALU
I$
Reg
D$
Reg
Schematically, this is what we want, but in reality stalls done “horizontally”
How to stall just part of pipeline?

## Slide 42: Data Hazard: Loads (3/4)
Stalled instruction converted to “bubble”, acts like nop
sub $t3,$t0,$t2
and $t5,$t0,$t4
or $t7,$t0,$t6
I$
ALU
Reg
D$
lw $t0, 0($t1)
ALU
I$
Reg
D$
Reg
bubble
bubble
bubble
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
sub $t3,$t0,$t2
I$
Reg
First two pipe stages stall by repeating stage one cycle later

## Slide 43: Data Hazard: Loads (4/4)
Slot after a load is called a load delay slot
  If that instruction uses the result of the load, then the hardware interlock will stall it for one cycle
  Letting the hardware stall the instruction in the delay slot is equivalent to putting an explicit nop in the slot (except the latter uses more code space)
Idea: Let the compiler put an unrelated instruction in that slot  no stall!
Notes: Micro processor without Interlocked Pipe Stages
1st version of MIPS did just that!
Version 2: added interlock: noops take space (in cache)…

## Slide 44: Code Scheduling to Avoid Stalls
Reorder code to avoid use of load result in the next instruction!
MIPS code for D=A+B; E=A+C;
# Method 1:
lw $t1, 0($t0)
lw $t2, 4($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
lw $t4, 8($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
# Method 2:
lw $t1, 0($t0)
lw $t2, 4($t0)
lw $t4, 8($t0)
add $t3, $t1, $t2
sw $t3, 12($t0)
add $t5, $t1, $t4
sw $t5, 16($t0)
Stall!
Stall!
13 cycles
11 cycles

## Slide 45: 3. Control Hazards
Branch determines flow of control
  Fetching next instruction depends on branch outcome
  Pipeline can’t always fetch correct instruction
    Still working on ID stage of branch
BEQ, BNE in MIPS pipeline
Simple solution Option 1: Stall on every branch until branch condition resolved
  Would add 2 bubbles/clock cycles for every Branch! (~ 20% of instructions executed)

## Slide 46: Stall => 2 Bubbles/Clocks
Where do we do the compare for the branch?
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 47: Control Hazard: Branching
Optimization #1:
  Insert special branch comparator in Stage 2
  As soon as instruction is decoded (Opcode identifies it as a branch), immediately make a decision and set the new value of the PC
  Benefit: since branch is complete in Stage 2, only one unnecessary instruction is fetched, so only one no-op is needed
  Side Note: means that branches are idle in Stages 3, 4 and 5

## Slide 48: One Clock Cycle Stall
Branch comparator moved to Decode stage.
I$
beq
Instr 1
Instr 2
Instr 3
Instr 4
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
ALU
Reg
D$
Reg
ALU
I$
Reg
D$
Reg
I
n
s
t
r.
O
r
d
e
r
Time (clock cycles)

## Slide 49: Control Hazards: Branching
Option 2: Predict outcome of a branch, fix up if guess wrong
  Must cancel all instructions in pipeline that depended on guess that was wrong
  This is called “flushing” the pipeline
Simplest hardware if we predict that all branches are NOT taken
  Why?

## Slide 50: Control Hazards: Branching
Option #3: Redefine branches
  Old definition: if we take the branch, none of the instructions after the branch get executed by accident
  New definition: whether or not we take the branch, the single instruction immediately following the branch gets executed (the branch-delay slot)
Delayed Branch means we always execute inst after branch
This optimization is used with MIPS

## Slide 51: Example: Nondelayed vs. Delayed Branch
add $1, $2, $3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Nondelayed Branch
add $1, $2,$3
sub $4, $5, $6
beq $1, $4, Exit
or $8, $9, $10
xor $10, $1, $11
Delayed Branch
Exit:
Exit:

## Slide 52: Control Hazards: Branching
Notes on Branch-Delay Slot
  Worst-Case Scenario: put a nop in the branch-delay slot
  Better Case: place some instruction preceding the branch in the branch-delay slot—as long as the changed doesn’t affect the logic of program
    Re-ordering instructions is common way to speed up programs
    Compiler usually finds such an instruction more than 50% of time
    Jumps also have a delay slot …

## Slide 53: Greater Instruction-Level Parallelism (ILP)
Deeper pipeline (5 => 10 => 15 stages)
  Less work per stage => shorter clock cycle
Multiple issue “superscalar”
  Replicate pipeline stages => multiple pipelines
  Start multiple instructions per clock cycle
  CPI < 1, so use Instructions Per Cycle (IPC)
  E.g., 4GHz 4-way multiple-issue
    16 BIPS, peak CPI = 0.25, peak IPC = 4
  But dependencies reduce this in practice
“Out-of-Order” execution
  Reorder instructions dynamically in hardware to reduce impact of hazards
§4.10 Parallelism and Advanced Instruction Level Parallelism

## Slide 54: In Conclusion
Pipelining increases throughput by overlapping execution of multiple instructions in different pipestages
Pipestages should be balanced for highest clock rate
Three types of pipeline hazard limit performance
  Structural (always fixable with more hardware)
  Data (use interlocks or bypassing to resolve)
  Control (reduce impact with branch prediction or branch delay slots)