## Slide 1: CS 110 Computer Architecture Lecture 18: Amdahl’s Law, Data-level Parallelism
Instructor:
Sören Schwertfeger
http://shtech.org/courses/ca/
School of Information Science and Technology SIST
ShanghaiTech University
Slides based on UC Berkley's CS61C

## Slide 2: New-School Machine Structures (It’s a bit more complicated!)
Parallel Requests
  Assigned to computer
  e.g., Search “Katz”
Parallel Threads
  Assigned to core
  e.g., Lookup, Ads
Parallel Instructions
  >1 instruction @ one time
  e.g., 5 pipelined instructions
Parallel Data
  >1 data item @ one time
  e.g., Add of 4 pairs of words
Hardware descriptions
  All gates @ one time
Programming Languages
Smart Phone
Warehouse Scale Computer
Software Hardware
Harness Parallelism &
Achieve High Performance
Logic Gates
Core
Core
…
Memory (Cache)
Input/Output
Computer
Cache Memory
Core
Instruction Unit(s)
Functional
Unit(s)
A3+B3
A2+B2
A1+B1
A0+B0
Today’s
Lecture

## Slide 3: Using Parallelism for Performance
Two basic ways:
  Multiprogramming
    run multiple independent programs in parallel
    “Easy”
  Parallel computing
    run one program faster
    “Hard”
We’ll focus on parallel computing for next few lectures

## Slide 4: Single-Instruction/Single-Data Stream (SISD)
Sequential computer that exploits no parallelism in either the instruction or data streams. Examples of SISD architecture are traditional uniprocessor machines
Processing Unit

## Slide 5: Single-Instruction/Multiple-Data Stream (SIMD or “sim-dee”)
SIMD computer exploits multiple data streams against a single instruction stream to operations that may be naturally parallelized, e.g., Intel SIMD instruction extensions or NVIDIA Graphics Processing Unit (GPU)

## Slide 6: Multiple-Instruction/Multiple-Data Streams (MIMD or “mim-dee”)
Multiple autonomous processors simultaneously executing different instructions on different data.
  MIMD architectures include multicore and Warehouse-Scale Computers
Instruction Pool
PU
PU
PU
PU
Data Pool

## Slide 7: Multiple-Instruction/Single-Data Stream (MISD)
Multiple-Instruction, Single-Data stream computer that exploits multiple instruction streams against a single data stream.
  Rare, mainly of historical interest only

## Slide 8: Flynn* Taxonomy, 1966
In 2013, SIMD and MIMD most common parallelism in architectures – usually both in same system!
Most common parallel processing programming style: Single Program Multiple Data (“SPMD”)
  Single program that runs on all processors of a MIMD
  Cross-processor execution coordination using synchronization primitives
SIMD (aka hw-level data parallelism): specialized function units, for handling lock-step calculations involving arrays
  Scientific computing, signal processing, multimedia (audio/video processing)
*Prof. Michael Flynn, Stanford

## Slide 9: Big Idea: Amdahl’s (Heartbreaking) Law
Speedup due to enhancement E is
Speedup w/ E = ----------------------
Exec time w/o E
Exec time w/ E
Suppose that enhancement E accelerates a fraction F (F <1) of the task by a factor S (S>1) and the remainder of the task is unaffected
Execution Time w/ E =
Speedup w/ E =
Execution Time w/o E x [ (1-F) + F/S]
1 / [ (1-F) + F/S ]

## Slide 10: Big Idea: Amdahl’s Law
Speedup = 1
(1 - F) + F
S
Non-speed-up part
Speed-up part
1
0.5 + 0.5
2
1
0.5 + 0.25
=
=
1.33
Example: the execution time of half of the program can be accelerated by a factor of 2. What is the program speed-up overall?

## Slide 11: Example #1: Amdahl’s Law
Consider an enhancement which runs 20 times faster but which is only usable 25% of the time
Speedup w/ E = 1/(.75 + .25/20) = 1.31
What if its usable only 15% of the time?
Speedup w/ E = 1/(.85 + .15/20) = 1.17
Amdahl’s Law tells us that to achieve linear speedup with 100 processors, none of the original computation can be scalar!
To get a speedup of 90 from 100 processors, the percentage of the original program that could be scalar would have to be 0.1% or less
Speedup w/ E = 1/(.001 + .999/100) = 90.99
Speedup w/ E = 1 / [ (1-F) + F/S ]

## Slide 12
If the portion of the program that can be parallelized is small, then the speedup is limited
The non-parallel portion limits the performance

## Slide 13: Strong and Weak Scaling
To get good speedup on a parallel processor while keeping the problem size fixed is harder than getting good speedup by increasing the size of the problem.
  Strong scaling: when speedup can be achieved on a parallel processor without increasing the size of the problem
  Weak scaling: when speedup is achieved on a parallel processor by increasing the size of the problem proportionally to the increase in the number of processors
Load balancing is another important factor: every processor doing same amount of work
  Just one unit with twice the load of others cuts speedup almost in half
Notes: Add load balancing example here – page 638

## Slide 14: Question
Suppose a program spends 80% of its time in a square root routine. How much must you speedup square root to make the program run 5 times faster?
A: 5
B: 16
C: 20
D: 100
E: None of the above
Speedup w/ E = 1 / [ (1-F) + F/S ]
Notes: Answer: E
Need infinitely fast to get to 5X
5 = 2.8
10 = 3.6
20 = 4.2
100 = 4.8

## Slide 15: SIMD Architectures
Data parallelism: executing same operation on multiple data streams
Example to provide context:
  Multiplying a coefficient vector by a data vector (e.g., in filtering)
y[i] := c[i]× x[i], 0 ≤ i < n
Sources of performance improvement:
  One instruction is fetched & decoded for entire operation
  Multiplications are known to be independent
  Pipelining/concurrency in memory access as well

## Slide 16: Intel “Advanced Digital Media Boost”
To improve performance, Intel’s SIMD instructions
  Fetch one instruction, do the work of multiple instructions
Notes: Vector of numbers => vector operation

## Slide 17: First SIMD Extensions: MIT Lincoln Labs TX-2, 1957

## Slide 18: Admin
Project Checkup:
  2 groups from lab 1 missing: today after lecture!
  Lab 2 and 3: everybody needs to attend
Project 2.x:
  Use git to share your work and collaborate
  New rule enforced:
    Every group member needs to have at least 2 commits and at least 25% of the # commits from his own PC.
    Penalty for violation: 10% off project score for violator!
    Will be posted also on piazza

## Slide 19: Intel SIMD Extensions
MMX 64-bit registers, reusing floating-point registers [1992]
SSE2/3/4, new 128-bit registers [1999]
AVX, new 256-bit registers [2011]
  Space for expansion to 1024-bit registers
Notes: Mmx 32 bit integer reg. FPU: 2 32 bit integers or 4 16bit integers ….
SSE Streaming SIMD Extensions
Advanced Vector Extensions

## Slide 20: XMM Registers
Architecture extended with eight 128-bit data registers: XMM registers
  x86 64-bit address architecture adds 8 additional registers (XMM8 – XMM15)
Notes: SSE: XMM registers

## Slide 21: Intel Architecture SSE2+ 128-Bit SIMD Data Types
64 63
64 63
64 63
32 31
32 31
96 95
96 95
16 15
48 47
80 79
122 121
64 63
32 31
96 95
16 15
48 47
80 79
122 121
16 / 128 bits
8 / 128 bits
4 / 128 bits
2 / 128 bits
Note: in Intel Architecture (unlike MIPS) a word is 16 bits
  Single-precision FP: Double word (32 bits)
  Double-precision FP: Quad word (64 bits)

## Slide 22: SSE/SSE2 Floating Point Instructions
xmm: one operand is a 128-bit SSE2 register
mem/xmm: other operand is in memory or an SSE2 register
{SS} Scalar Single precision FP: one 32-bit operand in a 128-bit register
{PS} Packed Single precision FP: four 32-bit operands in a 128-bit register
{SD} Scalar Double precision FP: one 64-bit operand in a 128-bit register
{PD} Packed Double precision FP, or two 64-bit operands in a 128-bit register
{A} 128-bit operand is aligned in memory
{U} means the 128-bit operand is unaligned in memory
{H} means move the high half of the 128-bit operand
{L} means move the low half of the 128-bit operand
Move does both load and store

## Slide 23: Packed and Scalar Double-Precision Floating-Point Operations
Packed
Scalar
Notes: Scalar: the same as normal FP but using the faster hardware…

## Slide 24: Example: SIMD Array Processing
for each f in array
f = sqrt(f)
for each f in array
{
load f to the floating-point register
calculate the square root
write the result from the register to memory
}
for each 4 members in array
{
load 4 members to the SSE register
calculate 4 square roots in one operation
store the 4 results from the register to memory
}
SIMD style

## Slide 25: Data-Level Parallelism and SIMD
SIMD wants adjacent values in memory that can be operated in parallel
Usually specified in programs as loops
for(i=1000; i>0; i=i-1)
x[i] = x[i] + s;
How can reveal more data-level parallelism than available in a single iteration of a loop?
Unroll loop and adjust iteration rate

## Slide 26: Looping in MIPS
Assumptions:
$t1 is initially the address of the element in the array with the highest address
$f0 contains the scalar value s
8($t2) is the address of the last element to operate on
CODE:
Loop: 1. l.d $f2,0($t1) ; $f2=array element
2. add.d $f10,$f2,$f0 ; add s to $f2
3. s.d $f10,0($t1) ; store result
4. addiu $t1,$t1,#-8 ; decrement pointer 8 byte
5. bne $t1,$t2,Loop ; repeat loop if $t1 != $t2

## Slide 27: Loop Unrolled
Loop: l.d $f2,0($t1)
add.d $f10,$f2,$f0
s.d $f10,0($t1)
l.d $f4,-8($t1)
add.d $f12,$f4,$f0
s.d $f12,-8($t1)
l.d $f6,-16($t1)
add.d $f14,$f6,$f0
s.d $f14,-16($t1)
l.d $f8,-24($t1)
add.d $f16,$f8,$f0
s.d $f16,-24($t1)
addiu $t1,$t1,#-32
bne $t1,$t2,Loop
NOTE:
Only 1 Loop Overhead every 4 iterations
This unrolling works if
loop_limit(mod 4) = 0
3. Using different registers for each iteration eliminates data hazards in pipeline

## Slide 28: Loop Unrolled Scheduled
Loop:l.d $f2,0($t1)
l.d $f4,-8($t1)
l.d $f6,-16($t1)
l.d $f8,-24($t1)
add.d $f10,$f2,$f0
add.d $f12,$f4,$f0
add.d $f14,$f6,$f0
add.d $f16,$f8,$f0
s.d $f10,0($t1)
s.d $f12,-8($t1)
s.d $f14,-16($t1)
s.d $f16,-24($t1)
addiu $t1,$t1,#-32
bne $t1,$t2,Loop
4 Loads side-by-side: Could replace with 4-wide SIMD Load
4 Adds side-by-side: Could replace with 4-wide SIMD Add
4 Stores side-by-side: Could replace with 4-wide SIMD Store
Notes: Even scalar code is faster this way…. :
Spread apart instructions that depend on each other!

## Slide 29: Loop Unrolling in C
Instead of compiler doing loop unrolling, could do it yourself in C
for(i=1000; i>0; i=i-1)
x[i] = x[i] + s;
Could be rewritten
for(i=1000; i>0; i=i-4) {
x[i] = x[i] + s;
x[i-1] = x[i-1] + s;
x[i-2] = x[i-2] + s;
x[i-3] = x[i-3] + s;
}
What is downside of doing it in C?
Notes: In C:
no scheduling
Portability

## Slide 30: Generalizing Loop Unrolling
A loop of n iterations
k copies of the body of the loop
Assuming (n mod k) ≠ 0
Then we will run the loop with 1 copy of the body (n mod k) times and with k copies of the body floor(n/k) times

## Slide 31: Example: Add Two Single-Precision Floating-Point Vectors
Computation to be performed:
vec_res.x = v1.x + v2.x;
vec_res.y = v1.y + v2.y;
vec_res.z = v1.z + v2.z;
vec_res.w = v1.w + v2.w;
SSE Instruction Sequence:
(Note: Destination on the right in x86 assembly)
movaps address-of-v1, %xmm0
// v1.w | v1.z | v1.y | v1.x -> xmm0
addps address-of-v2, %xmm0
// v1.w+v2.w | v1.z+v2.z | v1.y+v2.y | v1.x+v2.x -> xmm0
movaps %xmm0, address-of-vec_res
mov a ps : move from mem to XMM register, mem ory aligned, packed single precision
add ps : add from mem to XMM register, packed single precision
mov a ps : move from XMM register to mem, memory aligned, packed single precision
Notes: movaps: move aligned packed single (single float) : aligned on 16 bytes (128bit) – x86 also has unaligned access (slower)…
addps: add packed single operant, source and destination

## Slide 32: Intel SSE Intrinsics
Intrinsics are C functions and procedures for inserting assembly language into C code, including SSE instructions
  With intrinsics, can program using these instructions indirectly
  One-to-one correspondence between SSE instructions and intrinsics

## Slide 33: Example SSE Intrinsics
Vector data type:
_m128d
Load and store operations:
_mm_load_pd MOVAPD/aligned, packed double
_mm_store_pd MOVAPD/aligned, packed double
_mm_loadu_pd MOVUPD/unaligned, packed double
_mm_storeu_pd MOVUPD/unaligned, packed double
Load and broadcast across vector
_mm_load1_pd MOVSD + shuffling/duplicating
Arithmetic:
_mm_add_pd ADDPD/add, packed double
_mm_mul_pd MULPD/multiple, packed double
Corresponding SSE instructions:
Intrinsics:
Notes: CS267 Lecture 2
33

## Slide 34: Example: 2 x 2 Matrix Multiply
Ci,j = (A×B)i,j = ∑ Ai,k× Bk,j
2
k = 1
Definition of Matrix Multiply:
A1,1
A1,2
A2,1
A2,2
B1,1
B1,2
B2,1
B2,2
x
C1,1=A1,1B1,1 + A1,2B2,1
C1,2=A1,1B1,2+A1,2B2,2
C2,1=A2,1B1,1 + A2,2B2,1
C2,2=A2,1B1,2+A2,2B2,2
=
1
0
0
1
1
3
2
4
x
C1,1= 1*1 + 0*2 = 1
C1,2= 1*3 + 0*4 = 3
C2,1= 0*1 + 1*2 = 2
C2,2= 0*3 + 1*4 = 4
=

## Slide 35: Example: 2 x 2 Matrix Multiply
Using the XMM registers
  64-bit/double precision/two doubles per XMM reg
C1
C2
C1,1
C1,2
C2,1
C2,2
Stored in memory in Column order
B1
B2
Bi,1
Bi,2
Bi,1
Bi,2
A
A1,i
A2,i
C1
C2

## Slide 36: Example: 2 x 2 Matrix Multiply
Initialization
I = 1
C1
C2
0
0
0
0
B1
B2
B1,1
B1,2
B1,1
B1,2
A
A1,1
A2,1
_mm_load_pd: Stored in memory in Column order
_mm_load1_pd: SSE instruction that loads a double word and stores it in the high and low double words of the XMM register

## Slide 37
Initialization
I = 1
C1
C2
0
0
0
0
B1
B2
B1,1
B1,2
B1,1
B1,2
A
A1,1
A2,1
_mm_load_pd: Load 2 doubles into XMM reg, Stored in memory in Column order
_mm_load1_pd: SSE instruction that loads a double word and stores it in the high and low double words of the XMM register (duplicates value in both halves of XMM)
Example: 2 x 2 Matrix Multiply

## Slide 38: Example: 2 x 2 Matrix Multiply
First iteration intermediate result
I = 1
C1
C2
B1
B2
B1,1
B1,2
B1,1
B1,2
A
A1,1
A2,1
_mm_load_pd: Stored in memory in Column order
0+A1,1B1,1
0+A1,1B1,2
0+A2,1B1,1
0+A2,1B1,2
c1 = _mm_add_pd(c1,_mm_mul_pd(a,b1));
c2 = _mm_add_pd(c2,_mm_mul_pd(a,b2));
SSE instructions first do parallel multiplies and then parallel adds in XMM registers
_mm_load1_pd: SSE instruction that loads a double word and stores it in the high and low double words of the XMM register (duplicates value in both halves of XMM)

## Slide 39: Example: 2 x 2 Matrix Multiply
First iteration intermediate result
I = 2
C1
C2
0+A1,1B1,1
0+A1,1B1,2
0+A2,1B1,1
0+A2,1B1,2
B1
B2
B2,1
B2,2
B2,1
B2,2
A
A1,2
A2,2
_mm_load_pd: Stored in memory in Column order
c1 = _mm_add_pd(c1,_mm_mul_pd(a,b1));
c2 = _mm_add_pd(c2,_mm_mul_pd(a,b2));
SSE instructions first do parallel multiplies and then parallel adds in XMM registers
_mm_load1_pd: SSE instruction that loads a double word and stores it in the high and low double words of the XMM register (duplicates value in both halves of XMM)

## Slide 40: Example: 2 x 2 Matrix Multiply
Second iteration intermediate result
I = 2
C1
C2
B1
B2
B2,1
B2,2
B2,1
B2,2
A
A1,2
A2,2
_mm_load_pd: Stored in memory in Column order
C1,1
C1,2
C2,1
C2,2
c1 = _mm_add_pd(c1,_mm_mul_pd(a,b1));
c2 = _mm_add_pd(c2,_mm_mul_pd(a,b2));
SSE instructions first do parallel multiplies and then parallel adds in XMM registers
_mm_load1_pd: SSE instruction that loads a double word and stores it in the high and low double words of the XMM register (duplicates value in both halves of XMM)
A1,1B1,1+A1,2B2,1
A1,1B1,2+A1,2B2,2
A2,1B1,1+A2,2B2,1
A2,1B1,2+A2,2B2,2

## Slide 41: Example: 2 x 2 Matrix Multiply (Part 1 of 2)
#include <stdio.h>
// header file for SSE compiler intrinsics
#include <emmintrin.h>
// NOTE: vector registers will be represented in // comments as v1 = [ a | b]
// where v1 is a variable of type __m128d and // a, b are doubles
int main(void) {
// allocate A,B,C aligned on 16-byte boundaries
double A[4] __attribute__ ((aligned (16)));
double B[4] __attribute__ ((aligned (16)));
double C[4] __attribute__ ((aligned (16)));
int lda = 2;
int i = 0;
// declare several 128-bit vector variables
__m128d c1,c2,a,b1,b2;
// Initialize A, B, C for example
/* A = (note column order!)
1 0
0 1
*/
A[0] = 1.0; A[1] = 0.0; A[2] = 0.0; A[3] = 1.0;
/* B = (note column order!)
1 3
2 4
*/
B[0] = 1.0; B[1] = 2.0; B[2] = 3.0; B[3] = 4.0;
/* C = (note column order!)
0 0
0 0
*/
C[0] = 0.0; C[1] = 0.0; C[2] = 0.0; C[3] = 0.0;
Notes: Emmintrin extended multimedia intrinsics

## Slide 42: Example: 2 x 2 Matrix Multiply (Part 2 of 2)
// used aligned loads to set
// c1 = [c_11 | c_21]
c1 = _mm_load_pd(C+0*lda);
// c2 = [c_12 | c_22]
c2 = _mm_load_pd(C+1*lda);
for (i = 0; i < 2; i++) {
/* a =
i = 0: [a_11 | a_21]
i = 1: [a_12 | a_22]
*/
a = _mm_load_pd(A+i*lda);
/* b1 =
i = 0: [b_11 | b_11]
i = 1: [b_21 | b_21]
*/
b1 = _mm_load1_pd(B+i+0*lda);
/* b2 =
i = 0: [b_12 | b_12]
i = 1: [b_22 | b_22]
*/
b2 = _mm_load1_pd(B+i+1*lda);
/* c1 =
i = 0: [c_11 + a_11*b_11 | c_21 + a_21*b_11]
i = 1: [c_11 + a_21*b_21 | c_21 + a_22*b_21]
*/
c1 = _mm_add_pd(c1,_mm_mul_pd(a,b1));
/* c2 =
i = 0: [c_12 + a_11*b_12 | c_22 + a_21*b_12]
i = 1: [c_12 + a_21*b_22 | c_22 + a_22*b_22]
*/
c2 = _mm_add_pd(c2,_mm_mul_pd(a,b2));
}
// store c1,c2 back into C for completion
_mm_store_pd(C+0*lda,c1);
_mm_store_pd(C+1*lda,c2);
// print C
printf("%g,%g\n%g,%g\n",C[0],C[2],C[1],C[3]);
return 0;
}

## Slide 43: Inner loop from gcc –O -S
L2: movapd (%rax,%rsi), %xmm1 //Load aligned A[i,i+1]->m1
movddup (%rdx), %xmm0 //Load B[j], duplicate->m0
mulpd %xmm1, %xmm0 //Multiply m0*m1->m0
addpd %xmm0, %xmm3 //Add m0+m3->m3
movddup 16(%rdx), %xmm0 //Load B[j+1], duplicate->m0
mulpd %xmm0, %xmm1 //Multiply m0*m1->m1
addpd %xmm1, %xmm2 //Add m1+m2->m2
addq $16, %rax // rax+16 -> rax (i+=2)
addq $8, %rdx // rdx+8 -> rdx (j+=1)
cmpq $32, %rax // rax == 32?
jne L2 // jump to L2 if not equal
movapd %xmm3, (%rcx) //store aligned m3 into C[k,k+1]
movapd %xmm2, (%rdi) //store aligned m2 into C[l,l+1]

## Slide 44: And in Conclusion, …
Amdahl’s Law: Serial sections limit speedup
Flynn Taxonomy
Intel SSE SIMD Instructions
  Exploit data-level parallelism in loops
  One instruction fetch that operates on multiple operands simultaneously
  128-bit XMM registers
SSE Instructions in C
  Embed the SSE machine instructions directly into C programs through use of intrinsics
  Achieve efficiency beyond that of optimizing compiler