## Slide 1: CS 110 Computer Architecture Lecture 22: Operating Systems, Interrupts, Virtual Memory
Instructor:
Sören Schwertfeger
http://shtech.org/courses/ca/
School of Information Science and Technology SIST
ShanghaiTech University
Slides based on UC Berkley's CS61C

## Slide 2: CA so far…
Memory
CPU
Caches
MIPS Assembly
C Programs
#include <stdlib.h>
int fib(int n) {
return fib(n-1) + fib(n-2);
}
.foo
lw $t0, 4($r0)
addi $t1, $t0, 3
beq $t1, $t2, foo nop
Project 1
Project 2

## Slide 3: So how is this any different?
Keyboard
Screen
Storage

## Slide 4: Adding I/O
Memory
CPU
Caches
MIPS Assembly
C Programs
#include <stdlib.h>
int fib(int n) {
return fib(n-1) + fib(n-2);
}
.foo
lw $t0, 4($r0)
addi $t1, $t0, 3
beq $t1, $t2, foo nop
Project 1
Project 2
I/O (Input/Output)
Screen
Keyboard
Storage

## Slide 5: Raspberry Pi (< 300RMB on jd.com)
CPU+$s, etc.
Memory
Storage I/O
(Micro SD Card)
Serial I/O
(USB)
Network I/O
(Ethernet)
Screen I/O
(HDMI)

## Slide 6: It’s a real computer!

## Slide 7: But wait…
That’s not the same! When we run MARS, it only executes one program and then stops.
When I switch on my computer, I get this:
Yes, but that’s just software! The Operating System (OS)

## Slide 8: Well, “just software”
The biggest piece of software on your machine?
How many lines of code? These are guesstimates:
Codebases (in millions of lines of code). CC BY-NC 3.0 — David McCandless © 2013 http://www.informationisbeautiful.net/visualizations/million-lines-of-code/

## Slide 9: What does the OS do?
One of the first things that runs when your computer starts (right after firmware/ bootloader)
Loads, runs and manages programs:
  Multiple programs at the same time (time-sharing)
  Isolate programs from each other (isolation)
  Multiplex resources between applications (e.g., devices)
Services: File System, Network stack, etc.
Finds and controls all the devices in the machine in a general way (using “device drivers”)

## Slide 10: Agenda
Devices and I/O
OS Boot Sequence and Operation
Multiprogramming/time-sharing
Introduction to Virtual Memory

## Slide 11: Agenda
Devices and I/O
OS Boot Sequence and Operation
Multiprogramming/time-sharing
Introduction to Virtual Memory

## Slide 12: How to interact with devices?
Assume a program running on a CPU. How does it interact with the outside world?
Need I/O interface for Keyboards, Network, Mouse, Screen, etc.
  Connect to many types of devices
  Control these devices, respond to them, and transfer data
  Present them to user programs so they are useful
cmd reg.
data reg.
Operating System
Proc
Mem
PCI Bus
SCSI Bus

## Slide 13: Instruction Set Architecture for I/O
What must the processor do for I/O?
  Input: reads a sequence of bytes
  Output: writes a sequence of bytes
Some processors have special input and output instructions
Alternative model (used by MIPS):
  Use loads for input, stores for output (in small pieces)
  Called Memory Mapped Input/Output
  A portion of the address space dedicated to communication paths to Input or Output devices (no memory there)

## Slide 14: Memory Mapped I/O
Certain addresses are not regular memory
Instead, they correspond to registers in I/O devices
cntrl reg.
data reg.
0
0xFFFFFFFF
0xFFFF0000
address

## Slide 15: Processor-I/O Speed Mismatch
1GHz microprocessor can execute 1B load or store instructions per second, or 4,000,000 KB/s data rate
  I/O data rates range from 0.01 KB/s to 1,250,000 KB/s
Input: device may not be ready to send data as fast as the processor loads it
  Also, might be waiting for human to act
Output: device not be ready to accept data as fast as processor stores it
What to do?

## Slide 16: Processor Checks Status before Acting
Path to a device generally has 2 registers:
  Control Register, says it’s OK to read/write (I/O ready) [think of a flagman on a road]
  Data Register, contains data
Processor reads from Control Register in loop, waiting for device to set Ready bit in Control reg (0 => 1) to say it’s OK
Processor then loads from (input) or writes to (output) data register
  Load from or Store into Data Register resets Ready bit (1 => 0) of Control Register
This is called “Polling”

## Slide 17: I/O Example (polling)
Input: Read from keyboard into $v0
lui $t0, 0xffff #ffff0000 Waitloop: lw $t1, 0($t0) #control andi $t1,$t1,0x1 beq $t1,$zero, Waitloop lw $v0, 4($t0) #data
Output: Write to display from $a0
lui $t0, 0xffff #ffff0000 Waitloop: lw $t1, 8($t0) #control andi $t1,$t1,0x1 beq $t1,$zero, Waitloop sw $a0, 12($t0) #data
“Ready” bit is from processor’s point of view!
Notes: Synchronous control

## Slide 18: Cost of Polling?
Assume for a processor with a 1GHz clock it takes 400 clock cycles for a polling operation (call polling routine, accessing the device, and returning). Determine % of processor time for polling
  Mouse: polled 30 times/sec so as not to miss user movement
  Hard disk: assume transfers data in 16-Byte chunks and can transfer at 16 MB/second. Again, no transfer can be missed. (we’ll come up with a better way to do this)

## Slide 19: % Processor time to poll
Mouse Polling [clocks/sec]
  = 30 [polls/s] * 400 [clocks/poll] = 12K [clocks/s]
% Processor for polling:
  12*103 [clocks/s] / 1*109 [clocks/s] = 0.0012%
  => Polling mouse little impact on processor
Notes: was p 677 in book (not current edition)

## Slide 20: Clicker Time
  Hard disk: transfers data in 16-Byte chunks and can transfer at 16 MB/second. No transfer can be missed. What percentage of processor time is spent in polling (assume 1GHz clock)?
  A: 2%
  B: 4%
  C: 20%
  D: 40%
  E: 80%

## Slide 21: % Processor time to poll hard disk
Frequency of Polling Disk
  = 16 [MB/s] / 16 [B/poll] = 1M [polls/s]
Disk Polling, Clocks/sec = 1M [polls/s] * 400 [clocks/poll] = 400M [clocks/s]
% Processor for polling:
  400*106 [clocks/s] / 1*109 [clocks/s] = 40%
  => Unacceptable
  (Polling is only part of the problem – main problem is that accessing in small chunks is inefficient)

## Slide 22: What is the alternative to polling?
Wasteful to have processor spend most of its time “spin-waiting” for I/O to be ready
Would like an unplanned procedure call that would be invoked only when I/O device is ready
Solution: use exception mechanism to help I/O. Interrupt program when I/O ready, return when done with data transfer
Allow to register (post) interrupt handlers: functions that are called when an interrupt is triggered

## Slide 23: Interrupt-driven I/O
Label: sll $t1,$s3,2 addu $t1,$t1,$s5 lw $t1,0($t1)
add $s1,$s1,$t1 addu $s3,$s3,$s4 bne $s3,$s2,Label
Stack Frame
Stack Frame
Stack Frame
handler: lui $t0, 0xffff
lw $t1, 0($t0)
andi $t1,$t1,0x1
    lw $v0, 4($t0)
    sw $t1, 8($t0)
    ret
Interrupt(SPI0)
CPU Interrupt Table | 
SPI0 | handler
… | …
Handler Execution
Incoming interrupt suspends instruction stream
Looks up the vector (function address) of a handler in an interrupt vector table stored within the CPU
Perform a jal to the handler (needs to store any state)
Handler run on current stack and returns on finish (thread doesn’t notice that a handler was run)

## Slide 24: Agenda
Devices and I/O
OS Boot Sequence and Operation
Multiprogramming/time-sharing
Introduction to Virtual Memory

## Slide 25: What happens at boot?
When the computer switches on, it does the same as MARS: the CPU executes instructions from some start address (stored in Flash ROM)
CPU
PC = 0x2000 (some default value)
Address Space
0x2000:
addi $t0, $zero, 0x1000
lw $t0, 4($r0)
…
(Code to copy firmware into regular memory and jump into it)
Memory mapped

## Slide 26: What happens at boot?
When the computer switches on, it does the same as MARS: the CPU executes instructions from some start address (stored in Flash ROM)
1. BIOS: Find a storage device and load first sector (block of data)
2. Bootloader (stored on, e.g., disk): Load the OS kernel from disk into a location in memory and jump into it.
3. OS Boot: Initialize services, drivers, etc.
4. Init: Launch an application that waits for input in loop (e.g., Terminal/Desktop/...

## Slide 27: Launching Applications
Applications are called “processes” in most OSs.
Created by another process calling into an OS routine (using a “syscall”, more details later).
  Depends on OS, but Linux uses fork to create a new process, and execve to load application.
Loads executable file from disk (using the file system service) and puts instructions & data into memory (.text, .data sections), prepare stack and heap.
Set argc and argv, jump into the main function.

## Slide 28: Supervisor Mode
If something goes wrong in an application, it could crash the entire machine. And what about malware, etc.?
The OS may need to enforce resource constraints to applications (e.g., access to devices).
To help protect the OS from the application, CPUs have a supervisor mode bit.
  A process can only access a subset of instructions and (physical) memory when not in supervisor mode (user mode).
  Process can change out of supervisor mode using a special instruction, but not into it directly – only using an interrupt.
Notes: Jump back to supervisor mode: OS runs a timer which fires an interrupt

## Slide 29: Syscalls
What if we want to call into an OS routine? (e.g., to read a file, launch a new process, send data, etc.)
  Need to perform a syscall: set up function arguments in registers, and then raise software interrupt
  OS will perform the operation and return to user mode
Also, OS uses interrupts for scheduling process execution:
  OS sets scheduler timer interrupt then drops to user mode and start executing a user task, when interrupts triggers, switch into supervisor mode, select next task to execute (& set timer) and drop back to user mode.
This way, the OS can mediate access to all resources, including devices and the CPU itself.

## Slide 30: Agenda
Devices and I/O
OS Boot Sequence and Operation
Multiprogramming/time-sharing
Introduction to Virtual Memory

## Slide 31: Multiprogramming
The OS runs multiple applications at the same time.
But not really (unless you have a core per process)
Switches between processes very quickly. This is called a “context switch”.
When jumping into process, set timer interrupt.
  When it expires, store PC, registers, etc. (process state).
  Pick a different process to run and load its state.
  Set timer, change to user mode, jump to the new PC.
Deciding what process to run is called scheduling.

## Slide 32: Protection, Translation, Paging
Supervisor mode does not fully isolate applications from each other or from the OS.
  Application could overwrite another application’s memory.
  Also, may want to address more memory than we actually have (e.g., for sparse data structures).
Solution: Virtual Memory. Gives each process the illusion of a full memory address space that it has completely for itself.

## Slide 33: Agenda
Devices and I/O
OS Boot Sequence and Operation
Multiprogramming/time-sharing
Introduction to Virtual Memory

## Slide 34: “Bare” 5-Stage Pipeline
In a bare machine, the only kind of address is a physical address
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Physical Address

## Slide 35: Dynamic Address Translation
Motivation
  Multiprogramming, multitasking: Desire to execute more than one process at a time (more than one process can reside in main memory at the same time).
Location-independent programs
  Programming and storage management ease
=> base register – add offset to each address
Protection
  Independent programs should not affect
  each other inadvertently
=> bound register – check range of access
(Note: Multiprogramming drives requirement for resident supervisor (OS) software to manage context switches between multiple programs)
prog1
prog2
Physical Memory
OS

## Slide 36: Simple Base and Bound Translation
Load X
Program
Address Space
Bound
Register
Bounds
Violation?
Physical Memory
current
segment
Base
Register
+
Physical
Address
Logical
Address
Base and bounds registers are visible/accessible only when processor is running in supervisor mode
Base Physical Address
Segment Length
≤

## Slide 37: Base and Bound Machine
[ Can fold addition of base register into (register+immediate) address calculation using a carry-save adder (sums three numbers with only a few gate delays more than adding two numbers) ]
PC
Inst. Cache
D
Decode
E
M
Data Cache
W
+
Main Memory (DRAM)
Memory Controller
Physical Address
Physical Address
Physical Address
Physical Address
Data Bound Register
Data Base Register
≤
+
Logical Address
Bounds Violation?
Physical Address
Prog. Bound Register
Program Base Register
≤
+
Logical Address
Bounds Violation?

## Slide 38: Memory Fragmentation
As users come and go, the storage is “fragmented”.
Therefore, at some stage programs have to be moved
around to compact the storage.
OS
Space
16K
24K
24K
32K
24K
user 1
user 2
user 3
OS
Space
16K
24K
16K
32K
24K
user 1
user 2
user 3
user 5
user 4
8K
Users 4 & 5
arrive
Users 2 & 5
leave
OS
Space
16K
24K
16K
32K
24K
user 1
user 4
8K
user 3
free
Notes: Called Burping the memory.

## Slide 39: Paged Memory Systems
Processor-generated address can be split into:
Page tables make it possible to store the pages of a program non-contiguously.
0
1
2
3
0
1
2
3
Address Space
of User-1
Page Table
of User-1
1
0
2
3
page number offset
Physical Memory
A page table contains the physical address of the base of each page
Notes: Relaxes the contiguous allocation requirement.

## Slide 40: Private Address Space per User
Each user has a page table
Page table contains an entry for each user page
VA1
User 1
Page Table
VA1
User 2
Page Table
VA1
User 3
Page Table
Physical Memory
free
OS
pages
Notes: OS ensures that the page tables are disjoint.

## Slide 41: Where Should Page Tables Reside?
Space required by the page tables (PT) is proportional to the address space, number of users, ...
    Too large to keep in cpu registers
Idea: Keep PTs in the main memory
  Needs one reference to retrieve the page base address and another to access the data word
  => doubles the number of memory references!

## Slide 42: Page Tables in Physical Memory
VA1
User 1 Virtual Address Space
User 2 Virtual Address Space
PT User 1
PT User 2
VA1
Physical Memory
Notes: TLB cache

## Slide 43: In Conclusion
Once we have a basic machine, it’s mostly up to the OS to use it and define application interfaces.
Hardware helps by providing the right abstractions and features (e.g., Virtual Memory, I/O).